## Slide 1: Towards Battery-free HD Video Streaming
Saman Naderiparizi, Mehrdad Hessar, Vamsi Talla, Shyam Gollakota and Joshua R. Smith

## Slide 2: Snap Spectacle
Batteries add weight
Has heating issues
No video streaming

## Slide 3: Nest Camera
Needs to be plugged into power

## Slide 4: Grand Challenge
Design sticker form-factor battery-free camera tags

## Slide 5: Our Vision of Battery-free Cameras
Hub

## Slide 6: Challenge: Video Streaming is Power Hungry
At 720p 30fps grayscale
Image sensor: 85uW
ADC: 2mW
Digital Compression: 1W
Radios: 100mW
Total >1W
ADC
Digital
Compression
COM
…
…
…
…
Image Sensor

## Slide 7: We Take Inspiration from the Great Seal Bug
Radio
Tx
Rx
Hub
Tx
Rx
…
…
…
…
Image Sensor
Achieve Low-power Video Streaming

## Slide 8: Contributions
First demonstration of analog video backscatter that sends pixels directly to the antenna
Evaluated with multiple prototypes & simulations
  HD prototype with offline processing of 10fps grayscale 720p analog video backscatter at up to 14ft
  Spec out an IC that shows 30fps 720p and 1080p video at 252uW and 560uW respectively
  Live prototype of a 112x112 13fps video stream at 27ft

## Slide 9: Recorded Demo
Ultra Low Power HD Video Streaming

## Slide 10: Real-Time Demo
112 X 112 Resolution Video Streaming

## Slide 11: Demo 2
Single tone
transmitter
Low-resolution
camera
Receiver

## Slide 12: Technical Challenges
Analog Pixel Values
…
…
…
…
Image Sensor
Hub
Analog Pixel Values
Received Signal
Original
Image
Received
Image
Analog video has lower quality than digital video
Benefits of digital compression are lost in analog
  720p @ 30fps -> 221 Mbps uncompressed rate
  1080p @ 30fps -> 500 Mbps uncompressed rate

## Slide 13
Solution 1: Inspiration from Human Brain Signals
Neuron Spiking Signal
Analog
Pixels
Pulse-width
Modulation
Received Signal
Received Image

## Slide 14
Solution 1: Inspiration from Human Brain Signals
…
…
…
…
Image Sensor
-
+
Vmax
Vmin
Vmax
Vmin
PWM Signal
Overcome the curse of analog video
“Analog” Signal
We create pulse width modulated pixels using analog hardware
Comparator
Triangular Wave

## Slide 15: Technical Challenges
Analog signals are more
susceptible to noise
Compression
  Intra-frame compression
  Inter-frame compression
Analog video has lower quality than digital video
Benefits of digital compression are lost in analog

## Slide 16
Our Intra-Frame Compression
Reduces BW for 720p@30 analog video 70x
Adjacent pixels are fairly similar
We send video in zig-zag manner
Reduces average wireless bandwidth
Chart: Average Compression Ratio @30fps
| 360p | 720p | 1080p
Average Compression Ratio @ 30fps | 44 | 71 | 89
Across 100 HD-resolution YouTube videos

## Slide 17: Our Inter-Frame Compression Algorithm
What kind of operation can we perform?
Analog Domain
Low-power
Analog signals are more
susceptible to noise
Compression
  Intra-frame compression
  Inter-frame compression
Image Sensor
(2×2 Pixels)
Analog pixel output
Super-pixel average output
Averaging Operation

## Slide 18
Low-power analog computation  super-pixel
Distributed compression algorithm
Our Inter-Frame Compression Algorithm
5 super-pixel
5 super-pixel
Request super-pixel regions
100 px
100 px
Hub
Hub performs inter-frame comparison for compression

## Slide 19
Implementation
HD video streaming prototype
  Play HD videos from a PC to a DAC
  Custom backscatter switch
Low-resolution video streaming prototype
  112×112 grayscale low-power camera
  Low-power Igloo Nano FPGA
DAC
Our HD Prototype
Pixel Stream
Analog Signal

## Slide 20
Evaluation
We evaluate three main aspects
Quality of received videos
Our compression algorithm
Power consumption

## Slide 21
Chart: 
| 4 | 6 | 8 | 10 | 12 | 14 | 16
Series 1 | 7.2188 | 6.7692 | 5.9859 | 5.7751 | 4.8548 | 3.85 | 3.6595
Distance (in ft)
ENOB (bits)
Evaluation: HD Video Quality
Effective Number of Bits (ENOB)
Original Image (8 bits)
7 bits
4 bits
3 bits
We achieve about ~6 bits at distance of 10 feet

## Slide 22
Evaluation: HD Video Quality (Mobility)
Effective Number of Bits (ENOB)
Put our prototype antenna on a participant head
We asked participant to perform different poses
Chart: 
| Still | Moving Left and Right | Rotation | Talking | Moving Up and Down
Series 1 | 7.2188 | 6.3361 | 5.807 | 6.0326 | 5.5072
ENOB (bits)
We achieve ENOB greater than 5 for all poses

## Slide 23
Evaluation
We evaluate three main aspects
Quality of received videos
Our compression algorithm
Power consumption

## Slide 24
Evaluation: Inter-Frame Compression Algorithm
We record videos from a normal lab space
We change super-pixel size to evaluate our algorithm
PSNR (dB)
Compression Ratio

## Slide 25
Evaluation
We evaluate three main aspects
Quality of received videos
Our compression algorithm
Power consumption

## Slide 26
Evaluation: Power Consumption
We spec out an IC to emulate power consumption
Verilog camera interface, PWM converter, & RF switches
TSMC 65nm LP Process
Frame Rate | 60 fps | 30 fps | 10 fps
Video Quality | Power (𝜇W) | Power (𝜇W) | Power (𝜇W)
1080p (1920×1080) | 806.50 | 560.63 | 167.77
720p (1280×720) | 320.94 | 252.10 | 78.31
480p (640×480) | 126.88 | 106.78 | 36.71
360p (480×360) | 75.63 | 65.68 | 25.11

## Slide 27
Evaluation: Power Consumption
Harvested Power
(in mW)
Distance (in ft)
Chart: 
| 4 | 6 | 8 | 10 | 12 | 14 | 16
Series 1 | 2.245 | 0.9916 | 0.774 | 0.409 | 0.309 | 0.072 | 0.039
1080p @
60fps
1080p @
60fps
1080p @
30fps
720p @
60fps
720p @
30fps
360p @
30fps
480p @
10fps
Potential for battery-free video streaming

## Slide 28: Grand Challenge
Design sticker form-factor battery-free camera tags

## Slide 29: Trade-off and Road Ahead
Tradeoff between video quality and range
Explore advanced inter-frame compression
Build battery-free video streaming ASIC

## Slide 30: Contributions
First demonstration of “analog” video backscatter that sends pixels directly to the antenna
Evaluated with multiple prototypes & simulations
  HD prototype with offline processing of 10fps grayscale 720p analog video backscatter at up to 14ft
  Spec out an IC that shows 30fps 720p and 1080p video at 252uW and 560uW respectively
  Live prototype of a 112x112 13fps video stream at 27ft