## Slide 1: NetScatter: Enabling Large-Scale Backscatter Networks
Mehrdad Hessar*, Ali Najafi*, Shyam Gollakota
*Co-primary Student Authors

## Slide 2: Backscatter Communication
Ambient
Backscatter
SIGCOMM 2013
Best Paper
Award
Passive
Wi-Fi
NSDI 2016
Best Paper Award
LoRa
Backscatter
UbiComp 2017
Distinguished Paper Award
10 years operation with a button cell battery
Low-cost (10 – 20 cents)
Long-range coverage (up to km)

## Slide 3: Grand Challenge: Long-Range Backscatter Network

## Slide 4: NetScatter
First backscatter protocol supporting hundreds of concurrent transmissions
Distributed coding mechanism which works below noise floor and can be decoded using a single FFT
Network deployment of 256 devices using only 500 kHz
  Improvements in PHY-layer data rate (7-26x), link-layer throughput (14-62x) and network latency (15-67x)

## Slide 5: Outline
Distributed Chirp Spread Spectrum
Timing Synchronization
Near-Far Problem
Deployment of 256 devices

## Slide 6
Chirp Spread Spectrum
Supports high sensitivity and long-range
Bit ‘0’
Bit ‘1’
FFT Bin
Amplitude
FFT Bin
Amplitude

## Slide 7
Drawbacks of Chirp Spread Spectrum
Data rate vs range trade-off
TDMA network (each device 1 kbps)
  100 devices in network
  1000 devices in network
 10 bps
 1 bps

## Slide 8
Our Key Observation
Empty FFT Bins
Bit ‘1’
FFT Bin
Amplitude

## Slide 9
Our Idea: Distributed CSS
Alice: Bit ‘1’
Bob: Bit ‘1’
Alice: Bit ‘1’
Bob: Bit ‘0’
Alice: Bit ‘0’
Bob: Bit ‘1’
Alice: Bit ‘0’
Bob: Bit ‘0’
We assign each cyclic shift to a backscatter device
FFT Bin
Amplitude
FFT Bin
Amplitude
FFT Bin
Amplitude
FFT Bin
Amplitude
More power in the network  Higher network rate
Each device uses ON-OFF keying on cyclic-shift to communicate

## Slide 10
9
9
9
9
9
9
Network of Hundred Backscatter Devices
. . .
Access Point
FFT Bin
Amplitude
4
5
Single FFT

## Slide 11
How Many Concurrent Transmissions Can We Support?
Typical LoRa configuration
Uses 500 kHz BW
512 cyclic-shifts
Theoretically, we can support 512 concurrent transmissions using only 500 kHz BW

## Slide 12: Outline
Distributed Chirp Spread Spectrum
Timing Synchronization
Near-Far Problem
Deployment of 256 devices

## Slide 13
Practical Issues: Timing Synchronization
FFT Bin
Amplitude
FFT Bin
Amplitude
Causes interference between Alice and Bob
Freq
t
Freq
t
Not synchronized
Synchronized
Alice and Bob

## Slide 14
Timing Variation Across Devices
0
Time Variation (µs)
1-CDF
1
2
3
4
Hardware delay variations cause timing mismatch
2 µs delay translates to 1 FFT bin with 500kHz BW

## Slide 15
Timing Synchronization Solution
FFT Bin
Amplitude
3
4
We use every other cyclic-shift
Reduces concurrent transmissions from 512 to 256

## Slide 16: Outline
Distributed Chirp Spread Spectrum
Timing Synchronization
Near-Far Problem
Deployment of 256 devices

## Slide 17
Practical Issues: Near-Far Problem
Bob
Alice
Access Point
FFT Peak
FFT Bin
Amplitude

## Slide 18
Solution: Power-Aware Cyclic Shift Assignment
Similar power devices are clustered together
Near Devices
Far Devices
FFT Bin
Amplitude

## Slide 19
How to deal with changes in wireless channel?

## Slide 20
Solution: Power Adaptation Algorithm
Typical Backscatter Devices
NetScatter
  Each device uses AP’s query to self-adjusts its power
Switch Network
…
Achieve 0dB, -4dB and -10dB power gains
Starting power (-4 dB), increase power (0 dB), reduce power (-10 dB)

## Slide 21: Outline
Distributed Chirp Spread Spectrum
Timing Synchronization
Near-Far Problem
Deployment of 256 devices

## Slide 22
  Backscatter device
    Baseband: IGLOO nano FPGA
    Downlink: envelope detector
    and MSP430
    RF switch: ADG904
    Three levels power adjustment
  Access point
    USRP X-300 with UBX-40 daughterboard
    Co-located RX/TX antennas separated by 3 feet
Implementation

## Slide 23
Evaluation: Large-Scale Deployment
We deployed a network of 256 devices in an office building
Access Point
Backscatter Device
71’
80’

## Slide 24
Evaluation
We compared NetScatter with:
LoRa-Backscatter (9 kbps)
LoRa-Backscatter with rate adaptation

## Slide 25
1
16
32
64
96
128
160
192
224
256
0
50
100
150
200
250
# of Backscatter Devices
PHY Data Rate (kbps)
Evaluation: Network PHY Data-Rate
PHY data-rate improves by 7x - 26x
LoRa Backscatter (9 kbps)
LoRa Backscatter with Rate Adaptation
NetScatter

## Slide 26
Evaluation: Link-layer data-rate
Link-layer data-rate improves by 14x-62x
1
16
32
64
96
128
160
192
224
256
0
50
100
150
200
250
# of Backscatter Devices
Link-Layer
Data Rate (kbps)
LoRa Backscatter (9 kbps)
LoRa Backscatter with Rate Adaptation
NetScatter

## Slide 27
Evaluation: Network latency
Network latency improves by 15x-67x
1
16
32
64
96
128
160
192
224
256
0
500
1000
1500
2000
2500
# of Backscatter Devices
Network Latency (ms)
3000
3500
LoRa Backscatter (9 kbps)
LoRa Backscatter with Rate Adaptation
NetScatter

## Slide 28
NetScatter
We deployed a network of 256 devices in an office building
Access Point
Backscatter Device
71’
80’