## Slide 1: TinySDR
Mehrdad Hessar*, Ali Najafi*, Vikram Iyer, Shyam Gollakota
*Co-primary Student Authors

## Slide 2: IoT Ecosystem is Fast-Changing
2009
2015
???
2016
2017

## Slide 3: Academic community’s impact has been limited
Can’t easily scale IoT testbeds or develop
new low-power protocols
Each protocol requires a dedicated inflexible chip
Many are proprietary  Little room for innovation

## Slide 4: Ideal IoT Network Testbed
9
9
9
9
9
9
9
9
9
9
9
9
9
9
9
9
Battery-operated, duty-cycled SDR devices

## Slide 5: SDR must model constraints of IoT endpoints
Support duty-cycle  Ultra-low power sleep mode
Battery-operated  Low-power tx/rx mode
Ability to update PHY and MAC over-the-air wirelessly
Support interfaces with sensors

## Slide 6: Existing SDRs don’t satisfy these requirements
0.01
0.1
1
10
100
1000
10000
Sleep Power
Consumption (mW)
USRP
E310
USRP
B200
bladeRF
2.0
LimeSDR Mini
Pluto
SDR
uSDR
GalioT
TinySDR
N/A
N/A
N/A
Power Consumption (mW)
UBX 40
USRP
E310
USRP
B200
bladeRF
2.0
LimeSDR Mini
Pluto
SDR
uSDR
GalioT
TinySDR
0
1400
1200
1000
800
600
400
200
TX
RX
No
TX
Sleep power 10000 times too high
Radio module consumes high power for tx/rx
Require USB or Ethernet to update firmware

## Slide 7: TinySDR
First low-power SDR platform which supports over-the-air update for PHY and MAC layers
30uW in sleep mode
  10000x lower than existing platforms
Supports 900MHz and 2.4GHz ISM frequency bands, 4MHz bandwidth and digital/analog sensor interfaces
Has high sensitivities that match custom radio chipsets
  -126 dBm sensitivity for LoRa at 6 Kbps
  -94 dBm sensitivity for Bluetooth beacons

## Slide 8: TinySDR Platform Design
Physical layer design
MAC layer design
Over-the-air update

## Slide 9
Physical Layer Requirements
I/O supports 4MHz bandwidth
  Each I/Q sample 32bits  128Mbps
Real-time processing of 128Mbps data
  De/modulation running at line rate
Achieve these I/O and processing capabilities on a low-power device

## Slide 10
Low-Power FPGA for PHY
4-5 ms
> $40
Flash-Based
SRAM-Based
  Cost
  Boot Time
We use Lattice ECP5 SRAM-based FPGA
Operate FPGA at 64MHz
Has sufficient resources; LoRa Modulator (4%) Demodulator (11%)
20ms
$5-6
  Sleep
Built-in sleep mode
Requires shutoff

## Slide 11: TinySDR Platform Design
Physical layer design
MAC layer design
Over-the-air update

## Slide 12
End Device
Base station
Packet
Sleep
Rx slot 1
Rx slot 2
1 second
1 second
LoRa
FPGA for MAC leads to energy waste
FPGA ON: wasting 127mJ

## Slide 13
Our Solution: IoT MAC on Microcontroller
Big advantage of programmability
      C programming vs HDL programming
      Speed up innovation for MAC researchers
Enables energy efficient MAC protocol
Consumes only 2μW in sleep mode
  More than 10000 times less than FPGA

## Slide 14: TinySDR Platform Design
Physical layer design
MAC layer design
Over-the-air update

## Slide 15: Over-the-Air Update
9
9
9
9
9
9
9
9
9
9
9
9
9
9
9
9

## Slide 16
Dedicated Backbone Radio
Why dedicated radio?
  Support fail-safe mode if PHY or MAC layer have issue
Which radio?
  Supports long range up to a kilometer
  Low-power consumption in Rx/Tx modes
LoRa
  Challenge: Large FPGA/MCU firmware
  570KB FPGA file takes 14 min at 5kbps

## Slide 17
FPGA
Flash
Microcontroller
Memory
3
4
1
2
Our Solution: Compress Chunks of Firmware
Compression
1
2
3
4
. . .
1
  2
3
4
. . .

## Slide 18
Over-the-Air Update: Evaluation

## Slide 19
Over-the-Air Update: Evaluation
FPGA: LoRa
  Update LoRa 2100 times and BLE 5600 times
0.5
1
1.5
2
2.5
3
3.5
4
0
0.2
0.4
0.6
0.8
1
Duration (minutes)
CDF
FPGA: BLE
MCU: LoRa/BLE

## Slide 20
Sub-GHz I/Q
2.4 GHz I/Q
ADC
DAC
FPGA
Physical Layer
TinySDR Architecture
Microcontroller
MAC Protocols
LoRa Radio
Flash
Controller
Over-the-Air
Programming
Sensor
VMCU
VFPGA
VPA
.
.
.
VBat
Power
Management [30μW]

## Slide 21: TinySDR
First low-power SDR platform which supports over-the-air update for PHY and MAC layers
30uW in sleep mode
  10000x lower than existing platforms
Supports 900MHz and 2.4GHz ISM frequency bands, 4MHz bandwidth and digital/analog sensor interfaces
Has high sensitivities that match custom radio chipsets
  -126 dBm sensitivity for LoRa at 6 Kbps
  -94 dBm sensitivity for BLE beacon